## Slide 1: Cloud Computing Services
By
Arun

## Slide 2: Layout
TLDR
Deep Dive
Hands-on

## Slide 3: Disclaimer
Rapid Change is the new normal
arunvela@cdac.in
arunvel.wordpress.com
Arunvel Arunachalam [linkedin]
Mob - 9028825645

## Slide 13
1 RU = 1.75 inch
19 inch = Rack
23 inch = Rack

## Slide 34: Data Center Components
Basic Data Center facility systems:
  Physical space
  Raised flooring
  In-room electrical
  Standby power
  Data cabling
  Cooling
  Fire suppression

## Slide 35: Data Center Components
Physical Space
  Physical space refers to the footprint that Data Center-related items occupy. This generally applies to the overall area of the Data Center and its associated spaces, such as electrical rooms or storage areas. On a smaller scale this might refer to key dimensions within the Data Center, such as the external measurements of a server cabinet or aisle clearances.
Raised Flooring
  Raised flooring is an elevated grid system that is frequently installed in large Data Centers. Cooled air, electrical whips, and data cabling are routed through the space under the raised floor, promoting better air flow and enabling easier management of power and cable runs.
  Water pipes, fire suppressant cylinders, moisture detectors, and smoke detectors may be located here as well.

## Slide 36
  Raised flooring can vary in height from a few inches to several feet, or a few centimeters to several meters. In extreme cases they are as tall as the story of a building, enabling workers to walk upright under the plenum.
  Regardless of their height, the floors are typically composed of standard 2 foot (60 centimeter) square floor tiles.
  The tiles can vary in weight, strength, and finish depending upon their use.
  Tiles featuring either small perforations or large cut-out sections are placed in key locations to enable pass-through of air and cabling between the areas above and below the floor.

## Slide 37
In-Room Electrical
  In-room electrical refers to all power-related facilities within the Data Center. This normally includes electrical panels, conduits, and several types of receptacles.
  Power to this system usually comes from an outside commercial power source, namely your local utility company, and is likely conditioned at the company site. Voltage varies from one country to another.

## Slide 38
Cabling
  The cabling system is all structured cabling within the Data Center.
  Copper and fiber cabling are the typical media and are terminated via several types of connectors.
  Common components include fiber housings, patch panels, multimedia boxes
Cooling
  The cooling system refers to the chillers and air handlers used to regulate ambient temperature and control humidity within the Data Center.
  This system might incorporate the air conditioning system used to cool regular office space within the same building, known as house air, or might be independent of it.
  Individual server cabinets can also possess their own cooling measures, such as fans or water-cooling.

## Slide 39
Fire Suppression
  Fire suppression includes all devices associated with detecting or extinguishing a fire in the Data Center. The most obvious components are water-based sprinklers, gaseous fire suppression systems, and hand-held fire extinguishers. Others can include devices that detect smoke or measure air quality.
Other Infrastructure Components
  There are also some infrastructure items that do not strictly fall under the prior categories but are commonly found in server environments. These include leak detection devices, seismic mitigation, and physical security controls such as card readers and security cameras.

## Slide 40
Standby Power
  Standby power includes all backup power systems responsible for support of the Data Center's electrical load in the event that normal utility power fails for any reason.
  This system traditionally includes large batteries, known as an uninterruptible power source or uninterruptible power supply, and one or more generators.

## Slide 41: CRAC – Computer Room A/C

## Slide 53: Clone

## Slide 54: Template

## Slide 55: Snapshot

## Slide 56: Live Migration

## Slide 57: HA

## Slide 58: DRS